For Worldwide Release: September 2010

Release Number: 168PR10

Cat® D Series Mini Excavators Add More Performance and Operator Convenience to Predecessors' Quality and Reliability

The new Cat® D Series Mini Hydraulic Excavators—models 303.5D CR, 304D CR, 305D CR and 305.5D CR—are powerful, versatile, compact-radius machines that work comfortably in confined spaces and build on the quality design and reliability of their C Series predecessors—303C CR, 303.5C CR, 304C CR and 305C CR. With model designations that closely reflect their operating weights (3.5 to 5.5 metric tons), the new machines feature enhanced stability for greater productivity, a redesigned work-tool coupler, load-sensing hydraulics, and engines that meet U.S. EPA Tier-4 Interim and E.U. Stage-3A emissions regulations.

Models 303.5D CR and 304D CR are zero-tail-swing machines that keep the radius of the upper body within the width of the tracks; models 305D CR and 305.5D CR are compact-radius machines that limit upper-body tail swing over the tracks to 5.5 inches (140 mm) or less. Both designs reduce the machine's operating footprint and simplify the operator's job.

Increased-width undercarriages for the 303.5D CR and 304D CR and heavier counterweights for the 305D CR and 305.5D CR significantly enhance machine stability, allowing increased lift capacity, more effective use of reach and digging forces, increased capability when handling heavy work tools and improved machine balance for operator comfort.

A new pin-grabber-type coupler (with the new optional hydraulic operation) combines positive work-tool retention with a design that maintains tight tolerances between coupler and tool, significantly reducing wear.

A standard-equipment two-mode auxiliary-hydraulic system, complete with lines and quick connectors, can be switched between single-direction and bi-directional operation for effectively using work tools ranging from hydraulic breakers to augers. The implement hydraulic system is a responsive, load-sensing system resulting in low-effort pilot controls for optimum control and fast cycle times. In addition, refined main valves for the 305D CR and 305.5D CR further enhance hydraulic controllability.

Durable, functional design

Similar to large excavators, D Series booms feature a curved design for digging flexibility and fabricated-box construction for strength and durability. The independent-swing boom allows digging next to walls and obstructions, and an optional long digging arm for each model increases digging depth and lift height.

Digging arms also are equipped with brackets to facilitate installation of a versatile hydraulic thumb, and relief valves for the thumb are built into the main valve. Boom and digging-arm cylinders are end-dampened to reduce shock loads and material spills, and bucket rotation of more than 200 degrees not only assures improved material retention at height, but also makes flat-bottom trenching easier with less repositioning.

Enhancing overall capability of the new D Series models is a standard-equipment dozer blade that simplifies backfilling and clean-up chores. A float function allows the blade to follow ground contours with no operator correction. An optional angle-dozer blade, which can be angled 25 degrees to either side, further expands blade versatility.

Operator comfort and control

D-Series models are available with a two-post canopy operator's station, or with an optional enclosed cab that can be equipped with available air conditioning. The sealed cab provides premium standard features such as an efficient heater/defroster/ventilation system, sliding-door system for confined-area access, retractable front window (with gas-strut assist), removable lower-front window, sliding side window and a radio-ready package.

The spacious operator's compartment offers a comfortable suspension seat, adjustable wrist-rests, ample legroom and redesigned controls. The boom-swing function is now incorporated into the joystick controllers, and auxiliary-hydraulic controls also are positioned in the joysticks. An in-cab control allows switching the joysticks between an excavator and backhoe-type control pattern.

An automatic two-speed-travel feature shifts the drive system to meet changing torque and speed requirements, and a low-speed switch keeps the drive system in low range for precise-grading operations if desired. An automatic engine-idle feature reduces engine speed when hydraulic functions are inactive for four seconds, saving fuel and reducing sound levels and emissions.

Easy routine service

Extended routine-service intervals for D Series models save time and reduce operating costs: oil-impregnated sintered-alloy bearings in the boom and digging-arm linkages require grease only at 500-hour intervals; engine-oil changes are extended to 500 hours; and the hydraulic-oil change interval is 3,000 hours. A Cat S.O.SSM fluid-sampling port for hydraulic oil allows accurate, periodic assessment of fluid condition during its life.

A side-lifting hood allows access to the air filter, main control valve, auxiliary-hydraulic flow selector, fuel filter and hydraulic tank. The swing-out rear door provides an easy reach to engine-oil check/fill points, vertically mounted engine-oil filter, starter motor and alternator. In addition, the radiator and oil cooler are positioned for easy cleaning.

Basic Specifications

|  | 303.5D CR | 304D CR | 305D CR | 305.5D CR |
| --- | --- | --- | --- | --- |
| Operating Weight |  |  |  |  |
| Canopy— lb (kg) | 7,800 (3 540) | 8,500 (3 855) | 11,012 (4 995) | 11,696 (5 305) |
| Cab— lb (kg) | 8,160 (3 700) | 8,852 (4 015) | 11,365 (5 155) | 12,048 (5 465) |
| Net Power hp (kW): | 30 (22) | 39 (29) | 42 (31) | 47 (35) |
| Digging Depth: |  |  |  |  |
| Std. arm—ft (mm) | 9.50 ( 2 880) | 10.25 (3 130) | 10.75 (3 280) | 11.33 (3 470) |
| Long arm—ft (mm) | 10.33 (3 180) | 11.25 (3 430) | 12.10 (3 670) | 12.66 (3 870) |

For more information about the D Series Mini Hydraulic Excavators, customers should contact their local Cat dealer or visit www.cat.com.

# # #

CAT, CATERPILLAR, their respective logos, “Caterpillar Yellow” and the “Power Edge” trade dress, as well as corporate and product identity used herein, are trademarks of Caterpillar and may not be used without permission.

| Image Downloads Click On Images/Links Below for High Res **Most images are provided in .EPS format for high quality, appropriate software will be needed to open the zip file |
| --- |
| 303.5D CR | High Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C613838 Low Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C613838&imageType=2 |
| 304D CR | High Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C613836 Low Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C613836&imageType=2 |
| 305D CR | High Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C600772 Low Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C600772&imageType=2 |
| 305.5D CR | High Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C601123 Low Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C601123&imageType=2 |

| Press Inquiries | Americas: Sharon Holling Amber Santor Tel: 309-675-8995 Tel: 309-675-4693 Fax: 309-636-2738 Fax: 309-636-2738 Holling_Sharon_L@cat.com Santor_Amber_M@cat.com Europe, Africa, Middle East: Mia Karlsson Tel: +41-22-849-4662 Fax: +41-22-849-9993 Karlsson_Mia@cat.com |
| --- | --- |
| Reader Requests | www.cat.com/requestCatinfo |

# Text boxes

Press Release