For Worldwide Release:  August 2010

Release Number: 100PR10

Cat® B-Series 3 Loaders Feature Safety, Reliability and Convenience Refinements, Plus More Power for Models 242B3 and 257B3

The Cat® Skid Steer Loader (SSL) and Multi Terrain Loader (MTL) have earned the distinction of being tough, reliable machines that perform a variety of tasks competently, while providing exceptional convenience and control. Now, the new B-Series 3 loaders—SSL models 216B3, 226B3, 236B3, 242B3, 252B3 and MTL models 247B3 and 257B3—incorporate design refinements that make them even more capable, more reliable, safer and easier to operate. In addition, a larger engine and more powerful hydraulics for the 242B3 and 257B3 make these models "power-dense" machines that maintain a nimble size and excellent maneuverability.

Specific design refinements for all B-Series 3 models include a redesigned "dead-engine lower valve," single electronic control module (ECM), which is relocated for improved access and reliability, plus new ECM-enabled features. A heavy-duty battery (880 CCA) is now standard equipment on larger models, and a headliner is added to the optional Comfort Package.

The redesigned dead-engine lower valve further promotes safe operation by providing an easier-to-use, more-positive means of lowering the lift arms—allowing safe exit for the operator—if the machine should run out of fuel or the engine stall with the lift arms raised. The long cable and pull-type knob used to activate this system on B-Series 2 models has been replaced in B-Series 3 models with a low-effort, low-maintenance lever-action handle that acts directly on the hydraulic relief valve.

The new single ECM, relocated to the back of the cab (from the lower frame on the B-Series 2 models), provides easier access to fuses, relays and the Cat Electronic Technician port. The new ECM and its relocation also simplify wiring and reduce the number of connections.

New features enabled by the ECM include automatic glow-plug activation, expanded diagnostic capability and use of an optional on-demand cooling fan that spins the fan only as fast as required by the machine.  The optional fan improves fuel-efficiency, reduces sound levels and provides faster warm-up. For the model 226B3, the new ECM also allows automatic activation of the optional high-flow auxiliary-hydraulic system when a high-flow work tool is connected.

Expanded capability for 242B3 and 257B3

The basic redesign of the 242B3 SSL and 257B3 MTL involves adding substantial power—both engine and hydraulic—to allow these small-frame machines to perform as larger machines in confined spaces. Installing the Cat C3.4 DIT diesel engine, rated at 71 net horsepower (53 kW), gives these two models a 25-percent increase in net power, compared to their B-Series 2 counterparts, and a 28-percent boost in peak torque. The C3.4 DIT also runs at a lower, more-fuel-efficient speed, 2500 rpm, which is 500 rpm less than the B-Series 2 engine.

Complementing the more powerful engine in the 242B3 and 257B3 is a more capable hydraulic system, having a 6.4-gpm (24.2 lpm) increase in standard flow, from 15.6 to 22 gpm (59 to 83.3 lpm). Calculated hydraulic horsepower (the hydraulic power available to do work) is up by nearly 40 percent for these two new B-Series 3 models. This increase significantly improves the capability and efficiency of the 242B3 and 257B3 when handling standard-flow work tools, such as brush cutters, power box rakes and trenchers.

In addition, larger lift and tilt cylinders give these two new models a substantial gain in boom and bucket breakout force, from 13 to 19 percent, depending on model and circuit. Increased breakout forces provide enhanced performance in all basic functions—loading, lifting and digging.

Rated operating capacity also has been increased for the 242B3 and 257B3. The 242B3 is rated at 2,150 pounds (975 kg) at 50 percent of tipping load, or at 2,200 pounds (1 000 kg) when using an optional counterweight. The 257B3, when rated at 50 percent tipping load, has an operating capacity of 2,675 pounds ( 1 213 kg), which increases to 2,725 pounds (1 236 kg) with an optional counterweight. Standard rated operating capacity for the 257B3 is 1,870 pounds (848 kg) at 35 percent of tipping load.

The 242B3 and 257B3 also feature an engine-mounted air-conditioner compressor, which eliminates the hydraulic motor and plumbing required to drive the compressor on their B-Series 2 counterparts. The new configuration is a simpler design that uses fewer parts, reduces the number of hydraulic connections and lowers sound levels in the cab.

A new optional two-speed travel system gives the 242B3 top speeds of 7.1 and 10.6 mph (11.4 and 17.0 km/h) with 10 x 16.5 tires, and 7.7 and 11.4 mph (12.4 and 18.4 km/h) with larger 12 x 16.5 tires. Top speeds for the two-speed-equipped 257B3 are 6.9 and 10.0 mph (11.1 and 16.1 km/h).

#### Basic B-Series 3  SSL Specifications

|  | 216B3 | 226B3 | 236B3 | 242B3 | 252B3 |
| --- | --- | --- | --- | --- | --- |
| Net Power hp (kW) | 47 (35) | 56 (42) | 71 (53) | 71 (53) | 71 (53) |
| Operating Weight lb (kg) | 5,690 (2 581) | 5,822 (2 641) | 7,007 (3 178) | 7,008 (3 179) | 7,861 (3 565) |
| Rated Operating Capacity Std. @ 50% tip, lb (kg) | 1,400 (635) | 1,500 (680) | 1,950 (884) | 2,150 (975) | 2,650 (1 202) |
| Hyd. Flow (Std.) gpm (lpm) | 16 (61) | 16 (61) | 22 (83) | 22 (83) | 22 (83) |

##### Basic B-Series 3 MTL Specifications

|  | 247B3 | 257B3 |
| --- | --- | --- |
| Net Power hp (kW) | 56 (42) | 71 (53) |
| Operating Weight lb (kg) | 6,997 (3 174) | 8,060 (3 656) |
| Rated Operating Capacity Std. @ 50% tip, lb (kg) | 2,150 (975) | 2,675 (1 213) |
| Hyd. Flow (Std.) gpm (lpm) | 16 (61) | 22 (83) |

# # #

CAT, CATERPILLAR, their respective logos, “Caterpillar Yellow” and the “Power Edge” trade dress, as well as corporate and product identity used herein, are trademarks of Caterpillar and may not be used without permission.

| Image Downloads Click On Images/Links Below for High Res **Most images are provided in .EPS format for high quality, appropriate software will be needed to open the zip file |
| --- |
| 257B3 Multi Terrain Loader carrying sod | High Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C601054 Low Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C601054&imageType=2 |
| 257B3 Multi Terrain Loader with rake | High Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C601052 Low Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C601052&imageType=2 |
| 242B3 Skid Steer Loader carrying brick | High Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C606572 Low Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C606572&imageType=2 |
| 242B3 Skid Steer Loader loading gravel | High Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C606573 Low Res: http://xml.catmms.com/servlet/ImageServlet?imageId=C606573&imageType=2 |

| Press Inquiries | Americas: Sharon Holling Amber Santor Tel: 309-675-8995 Tel: 309-675-4693 Fax: 309-636-2738 Fax: 309-636-2738 Holling_Sharon_L@cat.com Santor_Amber_M@cat.com Europe, Africa, Middle East: Mia Karlsson Tel: +41-22-849-4662 Fax: +41-22-849-9993 Karlsson_Mia@cat.com |
| --- | --- |
| Reader Requests | www.cat.com/requestCatinfo |

# Text boxes

Press Release